## Slide 1: Design and Verification of NAND Flash based Memory Controller
Manjush Padmamma Venkatesha
Lakshmi Manoja Kavuri
Sumeeth Budhi Mahaveer
Yash Hiremath
ECE 571 Introduction to System Verilog
FINAL PROJECT

## Slide 2: TEAM CONTRIBUTION
Basic environment of design : Manjush
Design in SV : Manjush
Tested Design with Basic testbench : Manjush
Verification Plan : Sumeeth & Manjush
Deterministic approach of Verification : Manjush & Yash
Functional Verification : Sumeeth
Synthesized in DC : Sumeeth
Unit Testing in emulation : Manoja & Yash
Emulating design on velocesolo : Manoja & Yash

## Slide 3: Overview
Designed NAND Flash based Memory Controller (buffer and controller).
Unit testing of each module to check its functionality.
Verification approach
  Deterministic approach.
  Functional Verification.
Emulation in TBX Mode (BFM).

## Slide 4: Proposed objectives
Design, Verification & Emulation for NAND FLASH based Memory Controller
Operations to be performed:
  Reset
  Program Page
  Page Read

## Slide 5: Additional Improvements
Memory Design for Memory Controller
Additional operations :
  Block Erase
DC Synthesis
  Realized netlist
Verification :
  Implementation of scoreboard

## Slide 6: Design Aspects
Design of Memory Controller
  Buffer
  Controller
Top Design Model
  Memory Controller
  Memory

## Slide 7: Design Aspects
Operations Implemented
  Reset Memory Controller
  Block Erase
  Program Page
  Page Read

## Slide 8: Controller Design

## Slide 9: Memory Design
ValidEn & ALE/CLE/rEn/wEn=1
Status is asserted on transition of Memory read, Memory write, Memory erase states

## Slide 10: Buffer Design
Buffer Write
Buffer Read
Counter Implementation for Buffer Depth
Designed to handle data coherence
  Buffer overwrite
  Buffer read termination

## Slide 11
Block Diagram

## Slide 12: Verification Types
Deterministic Approach
Functional Verification

## Slide 13: Deterministic Approach
  Establish test environment
    Interface & Top Module Interactions
  Forcing input test vectors.
  Monitor DUT response on waveforms and transcript

## Slide 14
DUT
I
N
T
E
R
F
A
C
E
Test
Bench
Top Environment
PACKAGE
DETERMINISTIC APPROACH ENVIRONMENT

## Slide 15: Functional Verification
  Create test environment
    Interface
    Test Environment
    Top Environment
  Constraint Randomization
  Generating packets of test vectors
  Driving test vectors
  Monitor the response
  Assert the response and score it

## Slide 16
DUT
I
N
T
E
R
F
A
C
E
Top Environment
PACKAGE
Generator
Driver
MONITOR
SCORE BOARD
MAIL BOX
Transaction
MAIL BOX
Clk Reset
Test Environment
FUNCTIONAL VERIFICATION ENVIRONMENT

## Slide 17: Functional Verification
Verification approach using
  Constraint randomization
  Assertions
  Clocking
  Properties
  Interfaces

## Slide 18
Deterministic Approach Verification Results

## Slide 19
Functional Verification Results

## Slide 20: DC Synthesis
Used Synopsys Design Compiler (DC) to perform hardware synthesis.
This takes an RTL hardware description and a standard cell library as input and produces a gate level netlist as output.
The Output obtained is a complete structural description.
Generated using Tcl scripts.
DC synthesis flow

## Slide 21: Emulation of Design
Emulation on TBX Mode.
Environment - Veloce Solo emulator.
TBX mode emulation involves both the host link and co-simulation link.
Implementation-
  Interface and DUT - Veloce
  Untimed Testbench - Server
  Definition of tasks
    Communication to hvl
    Test vector generation

## Slide 22: Speed up achieved
To speedup, Simulators are event driven.
Speedup in TBX mode is obtained by reducing the number of interactions between server and the Veloce through the two links.
In Veloce mode ~ 1 minute
In Puresim mode = 1minute 3 seconds
Speedup achieved = 5%

## Slide 23
Memory Controller
NAND Flash Controller
Emulation Results

## Slide 24: Challenges Faced
Design:
  Timing control
  Region based event handling
  Designing using synthesizable constructs
Verification:
  Hierarchical test environment creation
  Hierarchical calls using handles
  Concurrent thread execution of test vectors
  Region based event handling
  Designing using synthesizable constructs
Emulation:
  Making the top hvl module untimed. (Implicit FSM approach)
  Complying with XRTL constraints on modeling tasks.

## Slide 25: Future Scope
Operations to be implemented
  Read ID
  Random Access
    Program Page
    Page Read
  Functional Verification
    Reference Model Design
    Assertion based BFM
    Checker
    Functional Coverage

## Slide 26: References
LATTICE Semiconductor NAND Flash Controller reference design manual.
Data sheet of Samsung K9F1G08R0A NAND Flash.
Design Compiler user guide.
Veloce user guide.
Veloce Languages and Communication Channels User Guide.
Veloce Reference manual.

## Slide 27: Your Queries Please ?